## Slide 1: UNIT-III Content Beyond Syllabus
The Multiplier Control Unit:
By Using Delay Method & Sequence Counter Method

## Slide 2: Design Methods for Hardwired Control
Sequence Counter Method:
  The most popular method conveniently employed for design of controllers with moderate complexity
Delay Element Method
  It depends on the use of clocked delay elements for generating the control signals
State Table Method
  It employs the traditional algorithmic approach to sequential circuit design using classical state table method.

## Slide 3: 1. Sequence Counter Method
Steps:
  Identify the distinct phases in the flowchart. Employ log p number of flip flops to handle p number distinct phases.
  Identify the maximum number of distinct steps, k, in each of the phases. Employ a mod k counter to generate control signals for each of the k steps.
  Design a combinational logic circuit to generate the sequence of control signals to control the micro operations of each phase; the signals for counter reset and phase control are also generated by the combinational logic.

## Slide 4: 1. Sequence Counter Method (cont..)

## Slide 5: 2. Delay Element Method
Control unit based on delay element method for the fetch cycle

## Slide 6: 3. State Table Method
The states Si (i=1,2…) of the controller generate the control signals to control the micro operations in the data path.
A controller in state ,say Si, on receiving the primary input signals Ij switches over to the state Si’ while generating the output signals {C’i}.
This set of output signals {C’i} execute the micro operations.

## Slide 7: 3. State Table Method (cont..)
It includes following steps:
  State assignment: It specifies the particular state of the controller at the specific time stamp.
  State Minimization: A set of states (Sa, Sb, …Sc ) can be merged into a single state S’ if Si and Sj (i≠j, i,j=a,b,c..) is pairwise compatible i.e. the output sequence {Oi} and {Oj} (that result from any input sequence I to the control unit in state Si and Sj as initial states) are identical whenever they are specified.
  State Encoding: State variables are defined and states are encoded in terms of state variables.

## Slide 8: Multiplier Unit (Hardware Implementation of Booth’s Algorithm)

## Slide 9: Multiplier Control Unit with Control Signals

## Slide 10: Control Signals for the 2’s Complement Multiplier