## Slide 1: UNIT-III
The Control Unit

## Slide 2: Syllabus Contents
Instruction Cycle & Micro Operations, Functional Requirements & Operations of the Control Unit, Block Schematic & Control Signals, Single Bus Processor Organization
Control Signal example with Micro Operations and Register Transfer.
Control Unit Design Methods - Hardwired Control – State Table Method, Design example – Multiplier CU.
Micro-Programmed Control - Basic Concepts, Microinstructions & Formats, Control Memory, Micro-Programmed Control Unit Schematic, Microinstruction Sequencing - Design Considerations,
Sequencing Techniques, Address Generation, Microinstruction Execution - A Taxonomy of Microinstructions, Microinstruction Encoding.

## Slide 3: Micro-Operations
A computer executes a program-Fetch/execute cycle.
Each instruction is executed during an instruction cycle made up of shorter subcycles (e.g., fetch, indirect, execute, interrupt).
The execution of each subcycle involves one or more shorter operations(or steps),that is, micro-operations.
Each step does very little atomic operation of CPU.
Micro-operations are the functional, or atomic, operations of a processor.
It helps in designing of control unit.

## Slide 4: Constituent Elements of a Program Execution

## Slide 5: Fetch - 4 Registers
Memory Address Register (MAR)
  Connected to address bus
  Specifies address for read or write op
Memory Buffer Register (MBR)
  Connected to data bus
  Holds data to write or last data read
Program Counter (PC)
  Holds address of next instruction to be fetched
Instruction Register (IR)
  Holds last instruction fetched

## Slide 6: Fetch Sequence
Address of next instruction is in PC
Address (MAR) is placed on address bus
Control unit issues READ command
Result (data from memory) appears on data bus
Data from data bus copied into MBR
PC incremented by 1 (in parallel with data fetch from memory)
Data (instruction) moved from MBR to IR
MBR is now free for further data fetches

## Slide 7: Fetch Sequence (symbolic)
t1: MAR <- (PC)
t2: MBR <- (memory)
PC <- (PC) +1
t3: IR <- (MBR)
(tx = time unit/clock cycle)
OR
t1: MAR <- (PC)
t2: MBR <- (memory)
t3: PC <- (PC) +1
IR <- (MBR)

## Slide 8: Rules for Clock Cycle Grouping
Proper sequence must be followed
  MAR <- (PC) must precede MBR <- (memory)
Conflicts must be avoided
  Must not read & write same register at same time
  MBR <- (memory) & IR <- (MBR) must not be in same cycle
Also: PC <- (PC) +1 involves addition
  Use ALU
  May need additional micro-operations

## Slide 9: Indirect Cycle
MAR <- (IRaddress) - address field of IR
MBR <- (memory)
IRaddress <- (MBRaddress)
MBR contains an address
IR is now in same state as if direct addressing had been used

## Slide 10: Interrupt Cycle
t1: MBR <-(PC)
t2: MAR <- save-address
PC <- routine-address
t3: memory <- (MBR)
This is a minimum
  May be additional micro-ops to get addresses
  Note: saving context is done by interrupt handler routine, not micro-ops

## Slide 11: Execute Cycle (ADD)
Different for each instruction
e.g. ADD R1,X - add the contents of location X to Register 1 , result in R1
    t1: MAR <- (IRaddress)
    t2: MBR <- (memory)
    t3: R1 <- R1 + (MBR)
Note: no overlap of micro-operations

## Slide 12: Execute Cycle (ISZ)
ISZ X - increment and skip if zero
    t1: MAR <- (IRaddress)
    t2: MBR <- (memory)
    t3: MBR <- (MBR) + 1
    t4: memory <- (MBR)
  if (MBR) == 0 then PC <- (PC) + 1
Notes:
  IF is a single micro-operation
  Micro-operations done during t4

## Slide 13: Execute Cycle (BSA)
BSA X - Branch and save address
  Address of instruction following BSA is saved in X
  Execution continues from X+1
    t1: MAR <- (IRaddress)
    MBR <- (PC)
    t2: PC <- (IRaddress)
    memory <- (MBR)
    t3: PC <- (PC) + 1

## Slide 14: Instruction Cycle
Each phase decomposed into sequence of elementary micro-operations
E.g. fetch, indirect, and interrupt cycles
Execute cycle
  One sequence of micro-operations for each opcode
Need to tie sequences together
Assume new 2-bit register
  Instruction cycle code (ICC) designates which part of cycle processor is in
    00: Fetch
    01: Indirect
    10: Execute
    11: Interrupt

## Slide 15: Flowchart for Instruction Cycle

## Slide 16: Functional Requirements
Define basic elements of processor
  ALU
  Registers
  Internal data pahs
  External data paths
  Control Unit
Describe types of micro-operations that processor performs
  Transfer data between registers
  Transfer data from register to external
  Transfer data from external to register
  Perform arithmetic or logical ops

## Slide 17: Functional Requirements (cont..)
Determine functions/operations control unit must perform
  Sequencing
    Causing the CPU to step through a series of micro-operations
  Execution
    Causing the performance of each micro-op
  This is done using Control Signals

## Slide 18: Block Schematic Diagram of Control Unit

## Slide 19: Control Signals
Clock
  One micro-instruction (or set of parallel micro-instructions) per clock cycle
Instruction register
  Op-code for current instruction
  Determines which micro-instructions are performed
Flags
  State of CPU
  Results of previous operations
From control bus
  Interrupts
  Acknowledgements

## Slide 20: Control Signals - output
Within CPU
  Cause data movement
  Activate specific functions
Via control bus
  To memory
  To I/O modules

## Slide 21: Data Paths and Control Signals

## Slide 22: Example Control Signal Sequence - Fetch
MAR <- (PC)
  Control unit activates signal to open gates between PC and MAR
MBR <- (memory)
  Open gates between MAR and address bus
  Memory read control signal
  Open gates between data bus and MBR

## Slide 23: Micro-operations and Control Signals

## Slide 24: Internal Organization
Usually a single internal bus
Gates control movement of data onto and off the bus
Control signals control data transfer to and from external systems bus
Temporary registers needed for proper operation of ALU

## Slide 25: Fundamental Concepts
Processor (CPU): the active part of the computer, which does all the work (data manipulation and decision-making).
Datapath: portion of the processor which contains hardware necessary to perform all operations required by the computer (the brawn).
Control: portion of the processor (also in hardware) which tells the datapath what needs to be done (the brain).

## Slide 26: Datapath
Datapath needs:
  access to storage (general purpose registers and memory)
  computational ability (ALU)
  helper hardware (local registers and PC)
Five stages of datapath (executing an instruction):
  Instruction Fetch (Increment PC)
  Instruction Decode (Read Registers)
  ALU (Computation)
  Memory Access
  Write to Registers
ALL instructions must go through ALL five stages.
Datapath is designed in hardware.

## Slide 27: Single Bus Organization
Data line
Address line
PC
MAR
MDR
Y
Internal processor bus
Memory bus
Z
MUX
A
ALU
B
Constant 4
Select
Add
Sub
XOR
:
ALU control lines
Carry-in
IR
RO
R(n–1)
:
:
TEMP
Instruction decoder and control logic
. . .
Control signals

## Slide 28: Single Bus Organization (cont..)
A single internal bus connects the ALU and all processor registers.
Gates and control movement of data onto and off the bus from each register.
Additional control signals control data transfer to and from the system (external) bus and the operation of the ALU.
Two temporary registers are needed for proper operation of ALU (Y: temporary input storage, Z: temporary output storage)

## Slide 29: Single Bus Organization (cont..)
Advantages:
  The use of common data paths simplifies the interconnection layout and the control of the processor.
  It saves space.
Disadvantage:
  Its control sequences are long as only one data item can be transferred over the bus in a clock cycle.

## Slide 30: Single Bus Organization (cont..)
e.g. Usage of temporary registers
  t1: MAR ← (IR(address))
  t2: MBR ← Memory
  t3: Y ← (MBR)
  t4: Z ← (AC) + (Y)
  t5: AC ← (Z)

## Slide 31: Register Transfer
Register to register transfer:
  For each register Ri, two control signals:
    Riin used to load the data on the bus into the register.
    Set Riin to 1 to load data from the processor bus into Ri.
    Riout to place the register’s contents on the bus.
    Set Riout to 1 to load contents of Ri on the bus.
    Riout=0Bus can be used for transferring data from other registers
  Example: To transfer contents of R1 to R4:
    Set R1out to 1. This places contents of R1 on the bus.
    Set R4in to 1. This loads data from the processor bus into R4.

## Slide 32: Register Transfer (cont..)
Y
Internal processor bus
Z
MUX
A
ALU
B
Constant 4
Select
Ri
X
Riin
X
Riout
Yin
X
X
Zin
Zout
X

## Slide 33: Register Transfer (cont..)
Input and output gating for one register bit
E.g. 4-bit register with D flip-flops:

## Slide 34: Arithmetic/Logic Operation
ALU: Performs arithmetic and logic operations on its A and B inputs.
To perform
R3  [R1] + [R2]:
  R1out, Yin
  R2out, SelectY, Add, Zin
  Zout, R3in
Y
Internal processor bus
Z
MUX
A
ALU
B
Constant 4
Select
Ri
X
Riin
X
Riout
Yin
X
X
Zin
Zout
X

## Slide 35: Arithmetic/Logic Operation (cont..)
If there are n operations, do we need n ALU control lines?
We could use encoding, which requires log2 n control lines for n operations. However, this will increase complexity and hardware (additional decoder needed).
A
ALU
B
Add
Sub
XOR
:
ALU control lines
Carry-in

## Slide 36: Reading a Word from Memory
E.g. Move (R1), R2 /* R2  [[R1]]
(opcode source destination)
  MAR  [R1]
  Start a Read operation on the memory bus
  Wait for the MFC response from the memory
  Load MDR from the memory bus
  R2  [MDR]
MDR has four
control signals:
  MDRin,
  MDRout,
  MDRinE
  MDRoutE.
Memory-bus data lines
MDR
X
MDRinE
X
MDRoutE
Internal processor bus
X
MDRin
X
MDRout

## Slide 37: Reading a Word from Memory (cont..)
E.g. Move (R1), R2 /* R2  [[R1]]
Sequence of control steps:
    R1out, MARin, Read
    MDRinE, WMFC
    MDRout, R2in
WMFC: Wait for arrival of MFC (Memory-Function-Completed) signal.
MFC: To accommodate variability in response time, the processor waits until it receives an indication that the Read/Write operation has been completed. The addressed device sets MFC to 1 to indicate this.

## Slide 38: Storing a Word in Memory
Move R2, (R1) /* [R1]  [R2]
Sequence of control steps:
  R1out, MARin
  R2out, MDRin, Write
  MDRoutE, WMFC

## Slide 39: Executing a Complete Instruction
E.g. Add (R3), R1 /* R1  [R1] + [[R3]]
Adds the contents of a memory location pointed
to by R3 to register R1.
Sequence of control steps:
  PCout, MARin, Read, Select4, Add, Zin
  Zout, PCin, Yin, WMFC
  MDRout, IRin
  R3out, MARin, Read
  R1out, Yin, WMFC
  MDRout, SelectY, Add, Zin
  Zout, R1in, End
Steps 1 – 3: Instruction fetch
Steps 4 – 7: Execution fetch

## Slide 40: Branch Instruction
A branch instruction replaces the contents of PC with the branch target address.
It is usually obtained by adding an offset X, which is given in the branch instruction, to the updated value of PC.
E.g. Unconditional branch
Sequence of control steps:
  PCout, MARin, Read, Select4, Add, Zin
  Zout, PCin, Yin, WMFC
  MDRout, IRin
  Offset-field-of- IRout , SelectY, Add, Zin
  Zout, PCin, End

## Slide 41: Branch Instruction (cont..)
For conditional branch we need to check the status of the condition codes before loading a new value into the PC.
E.g. Branch-on-negative(Branch<0)
Sequence of control steps:
  PCout, MARin, Read, Select4, Add, Zin
  Zout, PCin, Yin, WMFC
  MDRout, IRin
  Offset-field-of- IRout , SelectY, Add, Zin , If N=0 then End
  Zout, PCin, End
  Here, if N=0 the processor returns to step 1 immediately after step 4.
  If N=1. step 5 is performed to load a new value into the PC, thus performing the branch condition.

## Slide 42: Multiple-Bus Organization
Need:
  In Single-bus structure control sequences are long as only one data item can be transferred over the bus in a clock cycle.
  To reduce the number of steps needed, most commercial processors provide multiple internal paths that enable several transfers to take place in parallel.
Buses A and B are used to transfer source operands to the A and B inputs of ALU, and result transferred to destination over bus C.
The three-bus arrangement obviates the need for registers Y and Z.

## Slide 43: Multiple-Bus Organization (cont..) Three-Bus Structure

## Slide 44: Multiple-Bus Organization (cont..)
All general purpose registers are combined into a single block called register file with three ports:
  2 outputs allowing 2 registers to be accessed simultaneously and have their contents put on buses A and B, and
  1 input allowing data on bus C to be loaded into a third register.
Use of incrementer unit(for incrementing PC by 4)eliminates need to add 4 to PC using main ALU.
Constant 4 at ALU i/p multiplexer is still useful for incrementing other addresses such as memory addresses in LoadMultiple/ StoreMultiple instructions.

## Slide 45: Multiple-Bus Organization (cont..)
For the ALU, R=A (or R=B) means that its A (or B) input is passed unmodified to bus C.
E.g. Add R4, R5, R6 /* R6  [R4] + [R5]
  Adds the contents of R4 and R5 to R6.
Sequence of control steps:
  PCout, R=B, MARin, Read, IncPC
  WMFC
  MDRoutB, R=B, IRin
  R4outA, R5outB, SelectA, Add, R6in, End

## Slide 46: Control Systems
Two categories:
  Hardwired control
    Control unit is implemented using hardware.
    It physically connects all of the control lines to actual machine instructions.
    The control unit is essentially a state machine circuit.
    Its input logic signals are transformed into a set of output logic signals, which are the control signals.
  Micro programmed control
    Control unit is implemented using software.
    The logic of the control unit is specified by a microprogram.
    A microprogram consists of a sequence of instructions in a microprogramming language.
    These are very simple instructions that specify micro-operations.

## Slide 47: Hardwired Control (cont..)
A special digital circuit that uses:
  The bits from the opcode field in our instructions(IR)
  Bits from the Condition code flags
  Signals from the bus such as MFC, interrupt signals
  Signals from the Control step counter
Control signals
Clock
. . .
CLK
:
:
:
:
. . .
IR
Decoder/ encoder
External inputs
Condition codes
Control step counter

## Slide 48: Hardwired Control (cont..) Detailed Block Description

## Slide 49: Hardwired Implementation
Instruction register
  Op-code causes different control signals for each different instruction(INST1, INST2, ....)
  Unique logic for each op-code
  Decoder takes encoded input and produces single output
  n binary inputs and 2n outputs
Flags and control bus
  Each bit means something

## Slide 50: Hardwired Implementation (cont..)
Control unit inputs
Clock
  Repetitive sequence of pulses
  Useful for measuring duration of micro-ops
  Must be long enough to allow signal propagation
  Different control signals at different times within instruction cycle
  Need a counter with different control signals for T1, T2 etc.

## Slide 51: Hardwired Control (cont..) Generating Zin
Zin = T1 + T6 • ADD + T4 • BR + …
Generation of the Zin control signal for the processor

## Slide 52: Hardwired Control (cont..) Generating End
Generation of the END control signal for the processor

## Slide 53: Hardwired Control (cont..)
For memory operations, need a circuit which:
  Holds read/write until MFC received.
  Disables RUN until MFC received.
Advantage:
  Faster Speed
Disadvantages:
  Instruction set and Control logic are directly tied together using complicated circuits that are difficult to design and test.
  Inflexible to modify
  Expensive
  Complex sequencing & micro-operation logic

## Slide 54: Design Methods for Hardwired Control
Sequence Counter Method:
  The most popular method conveniently employed for design of controllers with moderate complexity
Delay Element Method
  It depends on the use of clocked delay elements for generating the control signals
State Table Method
  It employs the traditional algorithmic approach to sequential circuit design using classical state table method.

## Slide 55: State Table Method
The states Si (i=1,2…) of the controller generate the control signals to control the micro operations in the data path.
A controller in state ,say Si, on receiving the primary input signals Ij switches over to the state Si’ while generating the output signals {C’i}.
This set of output signals {C’i} execute the micro operations.

## Slide 56: State Table Method (cont..)
It includes following steps:
  State assignment: It specifies the particular state of the controller at the specific time stamp.
  State Minimization: A set of states (Sa, Sb, …Sc ) can be merged into a single state S’ if Si and Sj (i≠j, i,j=a,b,c..) is pairwise compatible i.e. the output sequence {Oi} and {Oj} (that result from any input sequence I to the control unit in state Si and Sj as initial states) are identical whenever they are specified.
  State Encoding: State variables are defined and states are encoded in terms of state variables.

## Slide 57: Multiplier Unit (Hardware Implementation of Booth’s Algorithm)

## Slide 58: Multiplier Control Unit with Control Signals

## Slide 59: Control Signals for the 2’s Complement Multiplier

## Slide 69: Microprogrammed Control
Developed by M.V. Wilkes in the early 1950’s
Proposed an idea that was organized & systematic and avoided the complications of hardwired implementation.
It is called micro-programming or firmware.
Control signals are generated by a program similar to machine language programs.

## Slide 70: Microprogrammed Control (cont..)
A microprogrammed control unit is a relatively simple logic circuit that is capable of :
  sequencing through microinstructions and
  Generating control signals to execute each microinstruction.
A sequence of microinstructions constitutes a microprogram.
Microprogram is an interpreter written in microcode that is stored in firmware(ROM, PROM, EEPROM) which is often called the control store.
The program converts zero’s and one’s into control signals.

## Slide 71: Microprogrammed Control (cont..)
Control word (CW) is a word whose individual bits represent the various control signals.
  Each of the control steps in the control sequence of an instruction defines a unique combination of 1s and 0s in the CW.
A sequence of CWs corresponding to the control sequence of machine instruction constitutes the microroutine for that instruction.
The individual control words in a microroutine are referred to as microinstructions.
  Each microinstruction specifies one or more microoperations that is performed.

## Slide 72: Example of Micro-instruction
E.g. ADD (R3), R1

## Slide 73: Basic organization of a microprogrammed control unit
To read CWs sequentially from the control store a microprogram counter(μPC) is used.
Every time the new instruction is loaded into IR.
The output of “starting address generator” is loaded into μPC.
μPC is then automatically incremented by the clock, causing successive microinstructions to be read from control store.
Hence the control signals are delivered to various parts of the processor in the correct sequence.

## Slide 74: Basic organization of a microprogrammed control unit
Micoprogrammed control is popular in Complex Instruction Set Architectures (CISC) because complex instruction sets require complex controllers that can more easily be implemented as microprograms.

## Slide 75: Conditional branch
The previous organization cannot handle the situation when the control unit is required to check the status of the condition codes or external inputs to choose between alternative courses of action.
Address
Microinstruction
0
PC
out
,
MAR
in
,
Read,
Select4,
Add,
Z
in
1
Z
out
,
PC
in
,
Y
in
,
WMF
C
2
MDR
out
,
IR
in
3
Branch
to
starting
address
of
appropriate
microroutine
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
25
If
N=0,
then
branch
to
microinstruction
0
26
Offset-field-of-IR
out
,
SelectY,
Add,
Z
in
27
Z
out
,
PC
in
,
End
Figure 7.17. Microroutine for the instruction Branch<0.

## Slide 76: Conditional branch(cont..)
Organization of the control unit to allow conditional branching in the microprogram.
Control
store
Clock
generator
Starting and
branch address
Condition
codes
inputs
External
CW
IR
m
P
C

## Slide 77: Microinstructions
A straightforward way to structure microinstructions is to assign one bit position to each control signal (total 42 control signals).
However, this is very inefficient:
  It results in long microinstructions(42-bit long).
  Only a few bits are set to 1(to be used for active gating) in any given microinstruction which means the available bit space is poorly used.
  Most signals are not needed simultaneously, and many signals are mutually exclusive.

## Slide 78: Microinstructions (cont..)
The length of the microinstruction can be reduced:
  All mutually exclusive signals are placed in the same group in binary coding.
  Thus at most one microoperation per group is specified at a time in any microinstruction.
  Binary encoding scheme is used to represent the signals within a group.
  Require a little more hardware-Decoding circuit
  Smaller control word(20 bits instead of 42 bits)

## Slide 79: Partial Format for field-encoded Micro-instruct-ions

## Slide 80: Microinstructions (cont..)
Enumerate the patterns of required signals in all possible microinstructions.
Each meaningful combination of active control signals can then be assigned a distinct code.
Such full encoding is likely to further reduce the length of microwords but also to increase the complexity of the required decoder circuits.

## Slide 81: Microinstructions (cont..)
Vertical organization:
  Highly encoded schemes that use compact codes to specify only a small number of control functions in each microinstruction.
  Slower operating speeds.
  Less hardware needed to handle the execution of microinstructions
Horizontal organization:
  Minimally encoded scheme in which many resources can be controlled with a single microinstruction.
  Useful when higher operating speed is required and machine structure allows parallel use of resources.

## Slide 82: Microinstructions (cont..)
Example of a horizontal organization scheme:
  PCout, MARin, Read, Select4, Add, Zin
  Zout, PCin, Yin, WMFC
  MDRout, IRin
  R3out, MARin, Read
  R1out, Yin, WMFC
  MDRout, SelectY, Add, Zin
  Zout, R1in, End
1 2 3 4 5 6 7 |  | 0 1 0 0 0 0 0 | 1 0 0 0 0 0 0 | 1 0 0 1 0 0 0 | 1 0 0 1 0 0 0 | 0 0 1 0 0 1 0 | 0 0 1 0 0 0 0 | 0 1 0 0 1 0 0 | 1 0 0 0 0 0 0 | 1 0 0 0 0 1 0 | 1 0 0 0 0 1 0 | 0 1 0 0 0 0 1 | 0 0 0 0 1 0 0 | 0 0 0 0 0 0 1 | 0 0 0 1 0 0 0 | 0 1 0 0 1 0 0 | 0 0 0 0 0 0 1 | 
PCin
PCout
End
MARin
Read
IRjn
Yin
Select
MDRout
Zout
Zin
R1out
R1in
Add
R3out
WMFC
Micro-instruction
..
..
Select=0: SelectY
Select=1: Select4

## Slide 83: Microprogram Sequencing
If all microprograms require only straightforward sequential execution of microinstructions except for branches, letting a μPC governs the sequencing would be efficient.
However, two disadvantages:
  Having a separate microroutine for each machine instruction results in a large total number of microinstructions and a large control store.
  Longer execution time because it takes more time to carry out the required branches.
Example: Add src, Rdst
  Four addressing modes: register, autoincrement, autodecrement, and indexed (with indirect forms).
  Combining simple microroutines by sharing common parts
  The microinstruction is located at the address indicated by the octal number above the upper right-hand corner of the box in the flowchart.

## Slide 84
Flowchart of a micro-program
e.g.
Add src, Rdst

## Slide 85: Microprogram Sequencing (cont..)
Branch-address Modification :
  Using Bit-ORing (e.g. By ORing LSB we get addr 170 for Indirect, 171 for direct)
  Conditional Branch
  Use of two next address fields(indirect & direct)
  Use of WMFC
Contents of IR:
  Assume 3 bits(no.10,9,8) for addressing mode:
  Bit 8: 0=Direct mode, 1= Indirect mode
  Bits 10,9: 00= Register
    01= Autoincrement
    10= Autodecrement
    11= Indexed

## Slide 86: Microprogram Sequencing (cont..)
Microinstruction for Add (Rsrc)+,Rdst.
  autoincrement mode; microinstruction at location 170 is not executed for this addressing mode

## Slide 87: Microinstructions with Next-Address Field
The microprogram we discussed requires several branch microinstructions, which perform no useful operation in the datapath.
A powerful alternative approach is to include an address field as a part of every microinstruction to indicate the location of the next microinstruction to be fetched.
Every microinstruction becomes a branch microinstruction , in addition to its other function.

## Slide 88: Microinstructions with Next-Address Field
Advantages:
  Separate branch microinstructions are virtually eliminated;
  Few limitations in assigning addresses to microinstructions.
  No need to keep track of sequential addresses. So µPC is replaced by Microinstruction Address Register (µAR).
Drawbacks:
  Additional bits for the address field (around 1/6th of control store capacity)

## Slide 89: Microinstructions with Next-Address Field
Microinstruction sequencing organization

## Slide 90: Implementation of the Microroutine
Micro routine using next-address field
e.g. Add (Rsrc)+,Rdst

## Slide 91: Tasks Done By Microprogrammed Control Unit
Microinstruction sequencing:
  Get the next microinstruction from the control memory.
Microinstruction execution:
  Generate the control signals needed to execute the microinstruction.
Must consider both together
Design Considerations:
  Size of microinstructions
  Address generation time
    Determined by instruction register
      Once per cycle, after instruction is fetched
    Next sequential address
      Common in most designed
    Branches
      Both conditional and unconditional

## Slide 92: Sequencing Techniques
Based on current microinstruction, condition flags, contents of IR, control memory address must be generated
Based on format of address information
  Two address fields
  Single address field
  Variable format

## Slide 93: Address Generation
Explicit | Implicit
Two-field | Mapping
Unconditional Branch | Addition
Conditional branch | Residual control

## Slide 94: Microinstruction Execution
The microinstruction cycle is the basic event on a microprogrammed processor.
Each cycle is made up of two events
  Fetch
    Determined by generation of microinstruction address
  Execute
Effect of the execution of a microinstruction:
  to generate control signals
  Some control points internal to processor
  Rest go to external control bus or other interface

## Slide 95: Control Unit Organization

## Slide 96: The Microinstruction Spectrum

## Slide 97: A Taxonomy of Microinstructions
Microinstructions can be classified in a variety of ways:-
  Vertical/horizontal
  Packed/unpacked
  Hard/soft microprogramming
  Direct/indirect encoding
Vertical/horizontal:
  relate to the relative width of microinstructions.
  a rule of thumb: vertical microinstructions have lengths in the range of 16 to 40 bits and horizontal microinstructions have lengths in the range of 40 to 100 bits.

## Slide 98: A Taxonomy of Microinstructions (cont..)
Packed/unpacked:
  The degree of packing relates to the degree of identification between a given control task and specific microinstruction bits.
  As the bits become more packed, a given number of bits contains more information. Thus, packing connotes encoding.
Hard/soft microprogramming
  Suggest the degree of closeness to the underlying control signals and hardware layout.
  Hard microprograms are generally fixed and committed to read-only memory.
  Soft microprograms are more changeable and are suggestive of user microprogramming.

## Slide 99: A Taxonomy of Microinstructions (cont..)
Direct/indirect encoding:
  Two approaches can be taken to organizing the encoded microinstruction into fields: functional and resource.
  Organize the format into independent fields. That is, each field depicts a set of actions (pattern of control signals) such that actions from different fields can occur simultaneously.
  Define each field such that the alternative actions that can be specified by the field are mutually exclusive. That is, only one of the actions specified for a given field could occur at a time.
  Direct encoding generally implies one level of decoding.
  Indirect encoding generally implies two levels of decoding.

## Slide 100: Encoding: Improvements over Wilkes
Wilkes had each bit directly produced a control signal or directly produced one bit of next address
More complex address sequencing schemes,
using fewer microinstruction bits, are possible
Require more complex sequencing logic module
Control word bits can be saved by encoding and subsequently decoding control information

## Slide 101: How to Encode
K different internal and external control signals
Wilkes’s:
  K bits dedicated
  2K control signals during any instruction cycle
Not all of these are used:
  Two sources cannot be gated to same destination
  Register cannot be source and destination
  Only one pattern presented to ALU at a time
  Only one pattern presented to external control bus at a time
Require Q < 2K which can be encoded with (log2Q )< K bits
Practically it is not done:
  As difficult to program as pure decoded (Wilkes) scheme
  Requires complex slow control logic module
Compromises
  More bits than necessary used
  Some combinations that are physically allowable are not possible to encode

## Slide 102: Specific Encoding Techniques
Microinstruction organized as set of fields
Each field contains code
Activates one or more control signals
Organize format into independent fields
  Field depicts set of actions (pattern of control signals)
  Actions from different fields can occur simultaneously
Alternative actions that can be specified by a field are mutually exclusive
  Only one action specified for field could occur at a time

## Slide 103: Microinstruction Encoding: Direct Encoding
The microinstruction is organized as a set of fields.
Each field contains a code, which, upon decoding, activates one or more control signals.
Thus, with N fields, N simultaneous actions are specified. Each action results in the activation of one or more control signals.

## Slide 104: Microinstruction Encoding: Indirect Encoding
One field is used to determine the interpretation of another field.
e.g. Consider an ALU that is capable of performing eight different arithmetic operations and eight different shift operations. A 1-bit field could be used to indicate whether a shift or arithmetic operation is to be used; a 3-bit field would indicate the operation.
This technique generally implies two levels of decoding, increasing propagation delays.

## Slide 105: Microinstruction Encoding: Indirect Encoding (cont..)